## Slide 1: 20-EECE-5117C/6017C—Aug. 23, 2017 1. Teams 2. Discussion of Documents from Monday 3. A very small embedded processor—team exercise Design of Architecture & Instruction Set for a Very Simple Processor; Getting to Know Your Team
Many embedded systems today contain powerful, multifunction processors.
But there are still many systems which employ processors with minimal instruction sets, limited register sets and memory, and low power usage.
The following slides describe a very simple processor. Work with your team to answer the questions about this processor. We will discuss your answers in class on Friday.
Please bring a team-produced document to hand in at the beginning of class Friday.
It does not need complete answers but it should show that your team has worked to come up with some reasonable ideas about what the answers should be.
Your team’s final answers will be due at the beginning of class on Monday.
You will also be asked to indicate how well your team worked together, who contributed what, and whether any adjustments in team assignments or working practices will be needed.

## Slide 2
The architecture on the following slide is for a very simple processor. Your team is tasked with designing an instruction set which would support the 3 given sample programs.
This exercise should help you to review architecture and programming concepts and it should also give you some practice working with a minimal set of instructions and registers.
Your team’s goal is to answer the following questions. Ask for help if necessary.
0--Implement logical functions (and,or,not) and 2’s c integer arithmetic (+,-,*,/) in an embedded processor, with the FEWEST POSSIBLE instructions implemented in hardware. Give the set of hardware instructions you will need.
1--using an expanding opcode, what should the instruction set be (specify op codes 0-6 and important op code 7 instruc.)? Note that you need to handle DATA MOVEMENT, LOGICAL/ARITHMETIC operations, and CONTROL statements.
2—Explain why your instructions will allow you to write the programs given on the slide.
3--What should be inside the ALU?
4--What signals must be generated in the control unit? what will each signal affect?
5--How will subroutines be handled? Where will the return address be stored?
6--How will interrupts be handled?
7—How will I/O be handled?
8—What is the memory size?

## Slide 3
ALU
M
MA
IR
AC
CF
MD
IA
IB
PC
ABUS (16)
OBUS (17)
BBUS (16)
ALU OUTPUT
M: memory
MA: memory address register
MD: memory data register
IR: instruction register
AC: accumulator
CF: carry flag (1 bit)
IA, IB: index registers (11 bit)
PC: program counter
Word addressable—all words 16 bits
Instruction format:
Op code
(3)
Addr Mode (2)
00:direct
01:indirect:
10: IA; 11:IB
Address
(11)
Functionality:
2's complement add, subtract, multiply, and divide, and, or, not
2. jumps (conditional and unconditional),
3. simple subroutine call and return
4. Interrupts
5. I/O
“Tiny Processor” Minimal hardware resources, high degree of functionality
What should instructions be?
(Hint: expanding opcode)
Some sample programs:
Let I,J be integers stored in memory. Read in a third integer X. If X >= 0, output I +J; else output I-J
Compute the sum of n numbers stored in an array in memory
Call a swap subroutine (SWAP(X,Y) that exchanges contents of mem locations X and Y). Remember that you need to return from the routine.
(also, need logical ops: In-put A,B. Output A xor B.)
***

## Slide 4: Some specific questions:
OP CODE DEFINITIONS: 000_______ 100_______ 111 (give ALL instruc): 001_______ 101_______
010_______ 110_______
011_______
Can the listed programs be implemented? Explain.
Functions inside ALU (give ALL):

## Slide 5
4. Control signals:
example: allow IR or AC on ABUS
5. How will “Jump to subroutine” be handled? Where will return address be stored?
How will interrupts be handled?
How will I/O be handled?
What is memory size? Explain.